## Slide 1: Chapter 10: DHCP
Routing & Switching
Notes: Cisco Networking Academy program
Routing & Switching
Chapter 10: DHCP

## Slide 2: Objectives
10.0 Introduction
10.1 Dynamic Host Configuration Protocol v4
10.2 Dynamic Host Configuration Protocol v6
10.3 Summary
Notes: Chapter 10

## Slide 3: Dynamic Host Configuration Protocol v4 DHCP
Notes: 10.1 Dynamic Host Configuration Protocol v4

## Slide 4: Introducing DHCPv4
DHCPv4 uses three different address allocation methods:
Manual Allocation – The administrator assigns a pre-allocated IPv4 address to the client, and DHCPv4 communicates only the IPv4 address to the device.
Automatic Allocation – DHCPv4 automatically assigns a static IPv4 address permanently to a device, selecting it from a pool of available addresses.
Dynamic Allocation – DHCPv4 dynamically assigns, or leases, an IPv4 address from a pool of addresses for a limited period of time chosen by the server, or until the client no longer needs the address. This method is the most commonly used.
Notes: 10.1.1.1 Introducing DHCPv4

## Slide 5: DHCPv4 Operation
Notes: 10.1.1.2 DHCPv4 Operation

## Slide 6: DHCPv4 Message Format
Notes: 10.1.1.3 DHCPv4 Message Format

## Slide 7: Format DHCPv4 Discover and Offer Messages
Notes: 10.1.1.4 DHCPv4 Discover and Offer Messages

## Slide 8: Configuring a DHCPv4 Server
A Cisco router running the Cisco IOS software can be configured to act as a DHCPv4 server. To set up DHCP:
  Exclude addresses from the pool.
  Set up the DHCP pool name.
  Define the range of addresses and subnet mask. Use the default-router command for the default gateway. Optional parameters that can be included in the pool – dns server, domain-name.
To disable DHCP, use the no service dhcp command.
Notes: 10.1.2.1 Configuring a DHCPv4 Server

## Slide 9: Verifying a DHCPv4 Server
Commands to verify DHCP:
  show running-config | section dhcp
  show ip dhcp binding
  show ip dhcp server statistics
On the PC, issue the ipconfig /all command.
Notes: 10.1.2.2 Verifying a DHCPv4 Server

## Slide 10: DHCPv4 Operation DHCPv4 Relay
  Using an IP helper address enables a router to forward DHCPv4 broadcasts to the DHCPv4 server. Acting as a relay.
Notes: 10.1.2.3 DHCPv4 Relay

## Slide 11: Configuring a DHCPv4 Client Configuring a Router as a DHCPv4 Client
Notes: 10.1.3.1 Configuring a Router as DHCPv4 Client

## Slide 12: Troubleshoot DHCPv4 Troubleshooting Tasks
Notes: 10.1.4.1 Troubleshooting Tasks

## Slide 13: Troubleshoot DHCPv4 Verifying the Router DHCPv4 Configuration
Notes: 10.1.4.2 Verify Router DHCPv4 Configuration

## Slide 14: Troubleshoot DHCPv4 Debugging DHCPv4
Notes: 10.1.4.3 Debugging DHCPv4

## Slide 15: Dynamic Host Configuration Protocol v6
Notes: 10.2 Dynamic Host Configuration Protocol v6

## Slide 16: SLAAC and DHCPv6 Stateless Address Autoconfiguration
Stateless Address Autoconfiguration (SLAAC) is a method in which a device can obtain an IPv6 global unicast address without the services of a DHCPv6 server.
ICMPv6 RS msg
ICMPv6 RA msg
Stateless as no server maintains network address information.
Notes: 10.2.1.1 Stateless Address Autoconfiguration (SLAAC)

## Slide 17: SLAAC and DHCPv6 SLAAC Operation
Using either
EUI-64
Randomly Generated
Using ICMPv6 neighbor solicitation msg with the target address of its own.
DAD
Notes: 10.2.1.2 SLAAC Operation

## Slide 18: SLAAC and DHCPv6 SLAAC and DHCPv6
Notes: 10.2.1.3 SLAAC and DHCPv6

## Slide 19: SLAAC and DHCPv6 SLAAC Option
Notes: 10.2.1.4 SLAAC Option

## Slide 20: SLAAC and DHCPv6 Stateless DHCP Option
1
Notes: 10.2.1.5 Stateless DHCP Option

## Slide 21: SLAAC and DHCPv6 Stateful DHCP Option
Notes: 10.2.1.6 Stateful DHCP Option

## Slide 22: SLAAC and DHCPv6 DHCPv6 Operations
Using reserved IPv6 multicast all-DHCP-servers-address FF02::1:2
Port 547
Server available for service
Stateless- INFORMATION REQUEST
Stateful - REQUEST
Notes: 10.2.1.7 DHCPv6 Operations

## Slide 23: Stateless DHCPv6 Configuring a Router as a Stateless DHCPv6 Server
Notes: 10.2.2.1 Configuring a Router as a Stateless DHCPv6 Server

## Slide 24: Stateless DHCPv6 Configuring a Router as a Stateless DHCPv6 Client
Notes: 10.2.2.2 Configuring a Router as a Stateless DHCPv6 Client

## Slide 25: Stateless DHCPv6 Verifying Stateless DHCPv6
Verify the stateless DHCP client using the following commands:
show IPv6 interface
debug ipv6 dhcp detail
Notes: 10.2.2.3 Verifying Stateless DHCPv6 Server and Client

## Slide 26: Stateful DHCPv6 Configuring a Router as a Stateful DHCPv6 Server
Notes: 10.2.3.1 Configuring a Router as a Stateful DHCPv6 Server

## Slide 27: Stateful DHCPv6 Verifying Stateful DHCPv6
Verify the stateful DHCPv6 server using the following commands:
show ipv6 dhcp pool
show ipv6 dhcp binding
Verify the stateful DHCPv6 client using the show ipv6 interface command.
Notes: 10.2.3.3. Verifying Stateful DHCPv6

## Slide 28: Stateful DHCPv6 Configuring a Router as a Stateful DHCPv6 Relay Agent
Notes: 10.2.3.4 Configuring a Router as a DHCPv6 Relay Agent

## Slide 29: Troubleshooting DHCPv6 Troubleshooting Tasks
Notes: 10.2.4.1 Troubleshooting Tasks

## Slide 30: Troubleshooting DHCPv6 Verifying the Router DHCPv6 Configuration
Notes: 10.2.4.2 Verify Router DHCPv6 Configuration

## Slide 31: Troubleshooting DHCPv6 Debugging DHCPv6
Notes: 10.2.4.3 Debugging DHCPv6