## Slide 1: Practice with 1’s and 2’s complement

## Slide 2
In 8 bit system, find the 1’s and 2’s complement of –(26)10
Find the decimal representation of (11010011)2s
Find the decimal representation of (11010111)1s
In 2’s complement system, find the negative value of (00010110) and what is it in decimal?

## Slide 3: Answer
1s: 111001012 and 2s: 111001102
-(45)10
-(40) 10
2s: 11101010 and in decimal -(22)10

## Slide 4
Using 7 bits to represent each number, write the representations of 23 and -23 in signed magnitude, 1’s complement integer and 2's complement integers

## Slide 5
No. | Sign magnitude | 1’s complement | 2’s complement
23 | 0010111 | 0010111 | 0010111
-23 | 1010111 | 1101000 | 1101001

## Slide 6: The following binary numbers are 4-bit 2's complement binary numbers. Which of the following operations generate overflow?
0110 + 0010
0111 + 1111

## Slide 7: Answer:
In 2’s complement:
a. 0110 + 0010 = (1000)2 = -810 (Overflow)
b. 0111 + 1111 = (0110)2 = 610 (No Overflow)

## Slide 8
Perform the subtraction with the following unsigned binary numbers by taking the 2's complement of the subtrahend. 11010 - 10000 (5 digits)

## Slide 9
First take 2's complement on 10000: 11111 - 10000 + 1 = 01111 + 1 = 10000 M = 11010
2's complement of N =+10000 ------- Sum =101010 Discard end carry Answer = 1010