## Slide 1: CSE 340 Computer Architecture Summer 2017 Understanding Performance
Notes: 8am class in 113 IST
Cabinet combination 5581
The projector combination (if needed, can tell if monitor screen comes awake with a key pad on it) is 1988
Choose one (central) projection mode, use resident PC, login with your CAC account, and go to slide mode (by touching on your “windows” window you can make it full screen-or not).
Second class at 9:45 in 104 Rackley – just behind Kern. Same cabinet combination. Have to turn on projector with remote control (in the cabinet) and lower the screen (controls on the wall behind the podium – light controls there as well).
Be sure to lock everything up when you are done!

## Slide 2: Performance Metrics
Purchasing perspective
  given a collection of machines, which has the
    best performance ?
    least cost ?
    best cost/performance?
Design perspective
  faced with design options, which has the
    best performance improvement ?
    least cost ?
    best cost/performance?
Both require
  basis for comparison
  metric for evaluation
Our goal is to understand what factors in the architecture contribute to overall system performance and the relative importance (and cost) of these factors
Notes: Or smallest/lightest
Longest battery life
Most reliable/durable (in space)

## Slide 3: Defining (Speed) Performance
Normally interested in reducing
  Response time (aka execution time) – the time between the start and the completion of a task
    Important to individual users
  Thus, to maximize performance, need to minimize execution time
  Throughput – the total amount of work done in a given time
    Important to data center managers
  Decreasing response time almost always improves throughput
performanceX = 1 / execution_timeX
  If X is n times faster than Y, then
performanceX execution_timeY
-------------------- = --------------------- = n
performanceY execution_timeX
Notes: Increasing performance requires decreasing execution time

## Slide 4: Performance Factors
Want to distinguish elapsed time and the time spent on our task
CPU execution time (CPU time) – time the CPU spends working on a task
  Does not include time waiting for I/O or running other programs
CPU execution time # CPU clock cycles
for a program for a program
= x clock cycle time
CPU execution time # CPU clock cycles for a program
for a program clock rate
= -------------------------------------------
Can improve performance by reducing either the length of the clock cycle or the number of clock cycles required for a program
or
Notes: Many techniques that decrease the number of clock cycles also increase the clock cycle time

## Slide 5: Review: Machine Clock Rate
Clock rate (MHz, GHz) is inverse of clock cycle time (clock period)
CC = 1 / CR
one clock period
10 nsec clock cycle => 100 MHz clock rate
5 nsec clock cycle => 200 MHz clock rate
2 nsec clock cycle => 500 MHz clock rate
1 nsec clock cycle => 1 GHz clock rate
500 psec clock cycle => 2 GHz clock rate
250 psec clock cycle => 4 GHz clock rate
200 psec clock cycle => 5 GHz clock rate
Notes: A clock cycle is the basic unit of time to execute one operation/pipeline stage/etc.

## Slide 6: Clock Cycles per Instruction
Not all instructions take the same amount of time to execute
  One way to think about execution time is that it equals the number of instructions executed multiplied by the average time per instruction
Clock cycles per instruction (CPI) – the average number of clock cycles each instruction takes to execute
  A way to compare two different implementations of the same ISA
# CPU clock cycles # Instructions Average clock cycles
for a program for a program per instruction
= x
 | CPI for this instruction class |  | 
 | A | B | C
CPI | 1 | 2 | 3

## Slide 7: Effective CPI
Computing the overall effective CPI is done by looking at the different types of instructions and their individual cycle counts and averaging
Overall effective CPI =  (CPIi x ICi)
i = 1
n
  Where ICi is the count (percentage) of the number of instructions of class i executed
  CPIi is the (average) number of clock cycles per instruction for that instruction class
  n is the number of instruction classes
The overall effective CPI varies by instruction mix – a measure of the dynamic frequency of instructions across one or many programs

## Slide 8: THE Performance Equation
Our basic performance equation is then
CPU time = Instruction_count x CPI x clock_cycle
Instruction_count x CPI
clock_rate
CPU time = -----------------------------------------------
or
These equations separate the three key factors that affect performance
  Can measure the CPU execution time by running the program
  The clock rate is usually given
  Can measure overall instruction count by using profilers/ simulators without knowing all of the implementation details
  CPI varies by instruction type and ISA implementation for which we must know the implementation details
Notes: Note that instruction count is dynamic – i.e., its not the number of lines in the code, but THE NUMBER OF INSTRUCTIONS EXECUTED

## Slide 9: Determinates of CPU Performance
CPU time = Instruction_count x CPI x clock_cycle
 | Instruction_count | CPI | clock_cycle
Algorithm |  |  | 
Programming language |  |  | 
Compiler |  |  | 
ISA |  |  | 
Processor organization |  |  | 
Technology |  |  | 
Notes: For class handout

## Slide 10: Determinates of CPU Performance
CPU time = Instruction_count x CPI x clock_cycle
 | Instruction_count | CPI | clock_cycle
Algorithm |  |  | 
Programming language |  |  | 
Compiler |  |  | 
ISA |  |  | 
Processor organization |  |  | 
Technology |  |  | 
X
X
X
X
X
X
X
X
X
X
X
X
Notes: For lecture

## Slide 11: Comparing and Summarizing Performance
Guiding principle in reporting performance measurements is reproducibility – list everything another experimenter would need to duplicate the experiment (version of the operating system, compiler settings, input set used, specific computer configuration (clock rate, cache sizes and speed, memory size and speed, etc.))
How do we summarize the performance for benchmark set with a single number?
  The average of execution times that is directly proportional to total execution time is the arithmetic mean (AM)
AM = 1/n  Timei
i = 1
n
  Where Timei is the execution time for the ith program of a total of n programs in the workload
  A smaller mean indicates a smaller average execution time and thus improved performance

## Slide 12: Other Performance Metrics
Power consumption – especially in the embedded market where battery life is important (and passive cooling)
  For power-limited applications, the most important metric is energy efficiency

## Slide 13: Aspects of CPU Execution Time
CPU Time = Instruction count x CPI x Clock cycle
Instruction Count I
Clock
Cycle
C
CPI
Depends on:
CPU Organization
Technology (VLSI)
Depends on:
Program Used
Compiler
ISA
CPU Organization
Depends on:
Program Used
Compiler
ISA
(Average
CPI)
T = I x CPI x C
I =Dynamic instruction
count executed

## Slide 14: CPU Execution Time: Example
A Program is running on a specific machine (CPU) with the following parameters:
  Total executed instruction count: 10,000,000 instructions Average CPI for the program: 2.5 cycles/instruction.
  CPU clock rate: 200 MHz. (clock cycle = 5x10-9 seconds) 5 nsec clock cycle => 200 MHz clock rate
What is the execution time for this program:
CPU time = Instruction count x CPI x Clock cycle
= 10,000,000 x 2.5 x 1 / clock rate
= 10,000,000 x 2.5 x 5x10-9
= .125 seconds
T = I x CPI x C

## Slide 15: Performance Comparison: Example
From the previous example: A Program is running on a specific machine with the following parameters:
  Total executed instruction count, I: 10,000,000 instructions
  Average CPI for the program: 2.5 cycles/instruction.
  CPU clock rate: 200 MHz.
Using the same program with these changes:
  A new compiler used: New instruction count 9,500,000
  New CPI: 3.0
  Faster CPU implementation: New clock rate = 300 MHZ
What is the speedup with the changes?
Speedup = (10,000,000 x 2.5 x 5x10-9) / (9,500,000 x 3 x 3.33x10-9 )
= .125 / .095 = 1.32
or 32 % faster after changes.
Speedup = Old Execution Time = Iold x CPIold x Clock cycleold
New Execution Time Inew x CPInew x Clock Cyclenew
Clock Cycle = 1/ Clock Rate

## Slide 16: Instruction Types & CPI: An Example
An instruction set has three instruction classes:
Two code sequences have the following instruction counts:
CPU cycles for sequence 1 = 2 x 1 + 1 x 2 + 2 x 3 = 10 cycles
CPI for sequence 1 = clock cycles / instruction count
= 10 /5 = 2
CPU cycles for sequence 2 = 4 x 1 + 1 x 2 + 1 x 3 = 9 cycles
CPI for sequence 2 = 9 / 6 = 1.5
Instruction class CPI
A 1
B 2
C 3
Instruction counts for instruction class
Code Sequence A B C
1 2 1 2
2 4 1 1
CPI = CPU Cycles / I
For a specific
CPU design

## Slide 17: Summary: Evaluating ISAs
Design-time metrics:
  Can it be implemented, in how long, at what cost?
  Can it be programmed? Ease of compilation?
Static Metrics:
  How many bytes does the program occupy in memory?
Dynamic Metrics:
  How many instructions are executed? How many bytes does the processor fetch to execute the program?
  How many clocks are required per instruction?
  How "lean" a clock is practical?
Best Metric: Time to execute the program!
depends on the instructions set, the processor organization, and compilation techniques.

## Slide 18: Next Lecture and Reminders
Next lecture
  MIPS non-pipelined datapath/control path review
    Reading assignment – PH, Chapter 5