## Slide 1: CSE 340 Computer Architecture Summer 2017 Basic MIPS Architecture Review
Notes: Other handouts
To handout next time

## Slide 2: The Processor: Datapath & Control
Our implementation of the MIPS is simplified
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
Generic implementation
  use the program counter (PC) to supply the instruction address and fetch the instruction from memory (and update the PC)
  decode the instruction (and read registers)
  execute the instruction
All instructions (except j) use the ALU after reading the registers
Fetch
PC = PC+4
Decode
Exec
Notes: memory reference use ALU to compute addresses
arithmetic use the ALU to do the require arithmetic
control use the ALU to compute branch conditions.

## Slide 3: High-level view of MIPS implementation
The MIPS computer can address 4 Gbyte of memory, from address 0x0000 0000 to 0xffff ffff
User memory is limited to locations below 0x7fff ffff
Text (program) storage always starts at 0x0040 0000
Data storage always starts at 0x1001 0000

## Slide 4: High-level view of MIPS implementation

## Slide 5: Clocking Methodologies
The clocking methodology defines when signals can be read and when they are written
  An edge-triggered methodology
Typical execution
  read contents of state elements
  send values through combinational logic
  write results to one or more state elements
State
element
1
State
element
2
Combinational
logic
clock
one clock cycle
Assumes state elements are written on every clock cycle; if not, need explicit write control signal
  write occurs only when both the write control is asserted and the clock edge occurs

## Slide 6: Clocking Methodologies
Combinational element: The elements that operates on data values, which means their output deepens on the current inputs. Example: AND gate, ALU.
State Elements: An element that contains state as has some internal storage. A state element has at least two inputs and one output. Example: register, a memory.

## Slide 7: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory
  updating the PC to hold the address of the next instruction
Read
Address
Instruction
Instruction
Memory
Add
PC
4
  PC is updated every cycle, so it does not need an explicit write control signal
  Instruction Memory is read every cycle, so it doesn’t need an explicit read control signal

## Slide 8: Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  reading two values from the Register File
    Register File addresses are contained in the instruction

## Slide 9: Executing R Format Operations
R format operations (add, sub, slt, and, or)
  perform the (op and funct) operation on values in rs and rt
  store the result back into the Register File (into location rd)
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
  The Register File is not written every cycle (e.g. sw), so we need an explicit write control signal for the Register File

## Slide 10: Executing Load and Store Operations
Load and store operations involves
  compute memory address by adding the base register (read from the Register File during decode) to the 16-bit signed-extended offset field in the instruction
  store value (read from the Register File during decode) written to the Data Memory
  load value, read from the Data Memory, written to the Register File
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
16
32

## Slide 11: Executing Branch Operations
Branch operations involves
  compare the operands read from the Register File during decode for equality (zero ALU output)
  compute the branch target address by adding the updated PC to the 16-bit signed-extended offset field in the instr
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)

## Slide 12: Executing Jump Operations
Jump operation involves
  replace the lower 28 bits of the PC with the lower 26 bits of the fetched instruction shifted left by 2 bits
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
address
26
4
28

## Slide 13: Creating a Single Datapath from the Parts
Assemble the datapath segments and add control lines and multiplexors as needed
Single cycle design – fetch, decode and execute each instructions in one clock cycle
  no datapath resource can be used more than once per instruction, so some must be duplicated (e.g., separate Instruction Memory and Data Memory, several adders)
  multiplexors needed at the input of shared elements with control lines to do the selection
  write signals to control writing to the Register File and Data Memory
Cycle time is determined by length of the longest path

## Slide 14: Fetch, R, and Memory Access Portions
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 15: Adding the Control
Selecting the operations to perform (ALU, Register File and Memory read/write)
Controlling the flow of data (multiplexor inputs)
I-Type:
op
rs
rt
address offset
31
25
20
15
0
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
Observations
  op field always
  in bits 31-26
  addr of registers
  to be read are always specified by the rs field (bits 25-21) and rt field (bits 20-16); for lw and sw rs is the base register
  addr. of register to be written is in one of two places – in rt (bits 20-16) for lw; in rd (bits 15-11) for R-type instructions
  offset for beq, lw, and sw always in bits 15-0
J-type:
31
25
0
op
target address

## Slide 16: Single Cycle Datapath with Control Unit
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: Note mux control inputs have been swapped (for three of the muxes) from the last picture to be consistent with the book.

## Slide 17: R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 18: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 19: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 20: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 21: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 22: Adding the Jump Operation
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Shift
left 2
0
1
Jump
32
Instr[25-0]
26
PC+4[31-28]
28
Notes: For lecture
Good exam questions
Add jalr rs,rd 0 rs 0 rd 0 9
jump to instr whose addr is in rs and save addr of next inst (PC+4) in rd
Add the PowerPC addressing modes of update addressing and indexed addressing (will have to expand the RegFile to be three read port and two write port)
Add andi, ori, addi - have to have both a signextend and a zeroextend and choose between the two, will have to augment the ALUop encoding (since can’t get the op information out of the funct bits as with R-type)
Add mult rs, rt with the result being left in hi|lo - so also include the mfhi and mflo instructions (will have to add a multiplier, the hi and lo registers and then a couple of muxes and their control).
Add barrel shifter

## Slide 23: Single Cycle Disadvantages & Advantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
  especially problematic for more complex instructions like floating point multiply
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
but
Is simple and easy to understand
Clk
lw
sw
Waste
Cycle 1
Cycle 2
Notes: In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.

## Slide 24: Multicycle Datapath Approach
Let an instruction take more than 1 clock cycle to complete
  Break up instructions into steps where each step takes a cycle while trying to
    balance the amount of work to be done in each step
    restrict each cycle to use only one major functional unit
  Not every instruction takes the same number of clock cycles
In addition to faster clock rates, multicycle allows functional units that can be used more than once per instruction as long as they are used on different clock cycles, as a result
  only need one memory – but only one memory access per cycle
  need only one ALU/adder – but only one ALU operation per cycle

## Slide 25: Multicycle Datapath Approach, con’t
At the end of a cycle
  Store values needed in a later cycle by the current instruction in an internal register (not visible to the programmer). All (except IR) hold data only between a pair of adjacent clock cycles (no write control signal needed)
  IR – Instruction Register MDR – Memory Data Register
  A, B – regfile read data registers ALUout – ALU output register
Address
Read Data
(Instr. or Data)
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
  Data used by subsequent instructions are stored in programmer visible registers (i.e., register file, PC, or memory)
Notes: Have to add multiplexors in front of several of the functional unit inputs because the functional units are shared by different instruction cycles.
Reading/writing to
  any of the internal registers or the PC occurs (quickly) at the end of a clock cycle
  reading/writing to the register file takes ~50% of a clock cycle since it has additional control and access overhead (reading can be done in parallel with decode)

## Slide 26: The Multicycle Datapath with Control Signals
Address
Read Data
(Instr. or Data)
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
Sign
Extend
Shift
left 2
ALU
control
Shift
left 2
ALUOp
Control
IRWrite
MemtoReg
MemWrite
MemRead
IorD
PCWrite
PCWriteCond
RegDst
RegWrite
ALUSrcA
ALUSrcB
zero
PCSource
1
1
1
1
1
1
0
0
0
0
0
0
2
2
3
4
Instr[5-0]
Instr[25-0]
PC[31-28]
Instr[15-0]
Instr[31-26]
32
28

## Slide 27: Multicycle Control Unit
Multicycle datapath control signals are not determined solely by the bits in the instruction
  e.g., op code bits tell what operation the ALU should be doing, but not what instruction cycle is to be done next
Must use a finite state machine (FSM) for control
  a set of states (current state stored in State Register)
  next state function (determined by current state and the input)
  output function (determined by current state and the input)
Combinational
control logic
State Reg
Inst
Opcode
Datapath
control
points
Next State
. . .
. . .
. . .

## Slide 28: The Five Steps of the Load Instruction
IFetch: Instruction Fetch and Update PC
Dec: Instruction Decode, Register Read, Sign Extend Offset
Exec: Execute R-type; Calculate Memory Address; Branch Comparison; Branch and Jump Completion
Mem: Memory Read; Memory Write Completion; R-type Completion (RegFile write)
WB: Memory Read Completion (RegFile write)
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
INSTRUCTIONS TAKE FROM 3 - 5 CYCLES!
Notes: As shown here, each of these five steps will take one clock cycle to complete.

## Slide 29: Multicycle Advantages & Disadvantages
Uses the clock cycle efficiently – the clock cycle is timed to accommodate the slowest instruction step
Multicycle implementations allow functional units to be used more than once per instruction as long as they are used on different clock cycles
but
Requires additional internal state registers, more muxes, and more complicated (FSM) control
Clk
Cycle 1
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type

## Slide 30: Single Cycle vs. Multiple Cycle Timing
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type
Clk
Single Cycle Implementation:
lw
sw
Waste
Cycle 1
Cycle 2
multicycle clock slower than 1/5th of single cycle clock due to state register overhead
Notes: Here are the timing diagrams showing the differences between the single cycle and multiple cycle.
In the multiple clock cycle implementation, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.

## Slide 31: Next Lecture and Reminders
Next lecture
  MIPS pipelined datapath review
    Reading assignment – PH, Chapter 6.1-6.3