## Slide 1: CSE 340 Computer Architecture Summer 2017 Basic MIPS Pipelining Review

## Slide 2: Multi-Cycle vs. Single-Cycle uArch
Advantages
Disadvantages
You should be very familiar with this right now

## Slide 3: Review: Single Cycle vs. Multiple Cycle Timing
Clk
Cycle 1
Multiple Cycle Implementation:
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type
Clk
Single Cycle Implementation:
lw
sw
Waste
Cycle 1
Cycle 2
multicycle clock slower than 1/5th of single cycle clock due to stage register overhead
Notes: Here are the timing diagrams showing the differences between the single cycle and multiple cycle.
In the multiple clock cycle implementation, we cannot start executing the store until Cycle 6 because we must wait for the load instruction to complete.
Similarly, we cannot start the execution of the R-type instruction until the store instruction has completed its execution in Cycle 9.
In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Consequently, the cycle time for the Single Cycle implementation can be five times longer than the multiple cycle implementation.

## Slide 4: Can We Do Better?
What limitations do you see with the multi-cycle design?
Limited concurrency
  Some hardware resources are idle during different phases of instruction processing cycle
  “Fetch” logic is idle when an instruction is being “decoded” or “executed”
  Most of the datapath is idle when a memory access is happening

## Slide 5: How Can We Make It Even Faster?
Split the multiple instruction cycle into smaller and smaller steps
Start fetching and executing the next instruction before the current one has completed
  Pipelining – (all?) modern processors are pipelined for performance
  Remember the performance equation: CPU time = CPI * CC * IC
Fetch (and execute) more than one instruction at a time
  Superscalar processing – stay tuned

## Slide 6: Can We Use the Idle Hardware to Improve Concurrency?
Goal: Concurrency  throughput (more “work” completed in one cycle)
Idea: When an instruction is using some resources in its processing phase, process other instructions on idle resources not needed by that instruction
  E.g., when an instruction is being decoded, fetch the next instruction
  E.g., when an instruction is being executed, decode another instruction
  E.g., when an instruction is accessing data memory (ld/st), execute the next instruction
  E.g., when an instruction is writing its result into the register file, access data memory for the next instruction

## Slide 7: Pipelining: Basic Idea
More systematically:
  Pipeline the execution of multiple instructions
  Analogy: “Assembly line processing” of instructions
Idea:
  Divide the instruction processing cycle into distinct “stages” of processing
  Ensure there are enough hardware resources to process one instruction in each stage
  Process a different instruction in each stage
    Instructions consecutive in program order are processed in consecutive stages
Benefit: Increases instruction processing throughput (1/CPI)
Downside: Start thinking about this…

## Slide 8: A Pipelined MIPS Processor
Start the next instruction before the current one has completed
  improves throughput - total amount of work done in a given time
  instruction latency (execution time, delay time, response time - time from the start of an instruction to its completion) is not reduced
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Cycle 7
Cycle 6
Cycle 8
sw
IFetch
Dec
Exec
Mem
WB
R-type
IFetch
Dec
Exec
Mem
WB
    clock cycle (pipeline stage time) is limited by the slowest stage
    for some instructions, some stages are wasted cycles
Notes: Latency = execution time (delay or response time) – the total time from start to finish of ONE instruction
For processors one important measure is THROUGHPUT (or the execution bandwidth) – the total amount of work done in a given amount of time
For memories one important measure is BANDWIDTH – the amount of information communicated across an interconnect (e.g., bus) per unit time; the number of operations performed per second (the WIDTH of the operation and the RATE of the operation)

## Slide 9: Single Cycle, Multiple Cycle, vs. Pipeline
Multiple Cycle Implementation:
Clk
Cycle 1
IFetch
Dec
Exec
Mem
WB
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
IFetch
Dec
Exec
Mem
lw
sw
IFetch
R-type
lw
IFetch
Dec
Exec
Mem
WB
Pipeline Implementation:
IFetch
Dec
Exec
Mem
WB
sw
IFetch
Dec
Exec
Mem
WB
R-type
Clk
Single Cycle Implementation:
lw
sw
Waste
Cycle 1
Cycle 2
Notes: Here are the timing diagrams showing the differences between the single cycle, multiple cycle, and pipeline implementations.
For example, in the pipeline implementation, we can finish executing the Load, Store, and R-type instruction sequence in seven cycles.

## Slide 10: Example: Execution of Four Independent ADDs
Multi-cycle: 4 cycles per instruction
Pipelined: 4 cycles per 4 instructions (steady state)
Time
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
Time

## Slide 11: An Ideal Pipeline
Goal: Increase throughput with little increase in cost (hardware cost, in case of instruction processing)
Repetition of identical operations
  The same operation is repeated on a large number of different inputs
Repetition of independent operations
  No dependencies between repeated operations
Uniformly partitionable suboperations
  Processing can be evenly divided into uniform-latency suboperations (that do not share resources)
Fitting examples: automobile assembly line, doing laundry

## Slide 12: MIPS Pipeline Datapath Modifications
What do we need to add/modify in our MIPS datapath?
  State registers between each pipeline stage to isolate them
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IFetch/Dec
Dec/Exec
Exec/Mem
Mem/WB
IF:IFetch
ID:Dec
EX:Execute
MEM:
MemAccess
WB:
WriteBack
System Clock
Sign
Extend
Notes: Note two exceptions to right-to-left flow
WB that writes the result back into the register file in the middle of the datapath
Selection of the next value of the PC, one input comes from the calculated branch address from the MEM stage
Only later instructions in the pipeline can be influenced by these two REVERSE data movements.
The first one (WB to ID) leads to data hazards.
The second one (MEM to IF) leads to control hazards.
All instructions must update some state in the processor – the register file, the memory, or the PC – so separate pipeline registers are redundant to the state that is updated (not needed).
PC can be thought of as a pipeline register: the one that feeds the IF stage of the pipeline. Unlike all of the other pipeline registers, the PC is part of the visible architecture state – its content must be saved when an exception occurs (the contents of the other pipe registers are discarded).

## Slide 13: Instruction Pipeline Throughput
200 400 600 800 1000 1200 1400 1600 1800
200 400 600 800 1000 1200 1400
800ps
800ps
800ps
200ps
200ps
200ps
200ps
200ps
200ps
200ps

## Slide 14: Enabling Pipelined Processing: Pipeline Registers
14
T
No resource is used by more than 1 stage!
IRD
PCF
PCD+4
PCE+4
nPCM
AE
BE
ImmE
AoutM
BM
MDRW
AoutW
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 15: Pipelined Operation Example
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 16: Pipelined Operation Example
16
Based on original figure from [P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 17: Illustrating Pipeline Operation: Operation View
MEM
EX
ID
IF
Inst4
WB
IF
MEM
IF
MEM
EX
t0
t1
t2
t3
t4
t5
ID
EX
IF
ID
IF
ID
Inst0
ID
IF
Inst1
EX
ID
IF
Inst2
MEM
EX
ID
IF
Inst3
WB
WB
MEM
EX
WB

## Slide 18: Illustrating Pipeline Operation: Resource View
I0
I0
I1
I0
I1
I2
I0
I1
I2
I3
I0
I1
I2
I3
I4
I1
I2
I3
I4
I5
I2
I3
I4
I5
I6
I3
I4
I5
I6
I7
I4
I5
I6
I7
I8
I5
I6
I7
I8
I9
I6
I7
I8
I9
I10
 | t0 | t1 | t2 | t3 | t4 | t5 | t6 | t7 | t8 | t9 | t10
IF |  |  |  |  |  |  |  |  |  |  | 
ID |  |  |  |  |  |  |  |  |  |  | 
EX |  |  |  |  |  |  |  |  |  |  | 
MEM |  |  |  |  |  |  |  |  |  |  | 
WB |  |  |  |  |  |  |  |  |  |  | 

## Slide 19: Control Signals in a Pipeline
For a given instruction
  same control signals as single-cycle, but
  control signals required at different cycles, depending on stage
  decode once using the same logic as single-cycle and buffer control signals until consumed
  or carry relevant “instruction word/field” down the pipeline and decode locally within each stage (still same logic)

## Slide 20: Pipelining the MIPS ISA
What makes it easy
  all instructions are the same length (32 bits)
    can fetch in the 1st stage and decode in the 2nd stage
  few instruction formats (three) with symmetry across formats
    can begin reading register file in 2nd stage
  memory operations can occur only in loads and stores
    can use the execute stage to calculate memory addresses
  each MIPS instruction writes at most one result (i.e., changes the machine state) and does so near the end of the pipeline (MEM and WB)
What makes it hard
  structural hazards: what if we had only one memory?
  control hazards: what about branches?
  data hazards: what if an instruction’s input operands depend on the output of a previous instruction?

## Slide 21: Graphically Representing MIPS Pipeline
Can help with answering questions like:
  How many cycles does it take to execute this code?
  What is the ALU doing during cycle 4?
  Is there a hazard, why does it occur, and how can it be fixed?
ALU
IM
Reg
DM
Reg

## Slide 22: Why Pipeline? For Performance!
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Once the pipeline is full, one instruction is completed every cycle, so CPI = 1
Time to fill the pipeline

## Slide 23: Can Pipelining Get Us Into Trouble?
Yes: Pipeline Hazards
  structural hazards: attempt to use the same resource by two different instructions at the same time
  data hazards: attempt to use data before it is ready
    An instruction’s source operand(s) are produced by a prior instruction still in the pipeline
  control hazards: attempt to make a decision about program control flow before the condition has been evaluated and the new PC target address calculated
    branch instructions
Can always resolve hazards by waiting
  pipeline control must detect the hazard
  and take action to resolve hazards
Notes: Note that data hazards can come from R-type instructions or lw instructions

## Slide 24: A Single Memory Would Be a Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
lw
Inst 1
Inst 2
Inst 4
Inst 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Reading data from memory
Reading instruction from memory
Fix with separate instr and data memories (I$ and D$)

## Slide 25: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
add $1,
Inst 1
Inst 2
add $2,$1,
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Notes: For class handout

## Slide 26: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 1
Inst 2
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix register file access hazard by doing reads in the second half of the cycle and writes in the first half
add $1,
add $2,$1,
clock edge that controls register writing
clock edge that controls loading of pipeline state registers
Notes: For lecture
Define register reads to occur in the second half of the cycle and register writes in the first half

## Slide 27: Register Usage Can Cause Data Hazards
I
n
s
t
r.
O
r
d
e
r
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
Read before write data hazard
Notes: For class handout

## Slide 28: Register Usage Can Cause Data Hazards
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Read before write data hazard
Notes: For lecture

## Slide 29: Loads Can Cause Data Hazards
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
Load-use data hazard
Notes: Note that lw is just another example of register usage (beyond ALU ops)

## Slide 30: One Way to “Fix” a Data Hazard
stall
stall
I
n
s
t
r.
O
r
d
e
r
add $1,
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$1,$7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Can fix data hazard by waiting – stall – but impacts CPI

## Slide 31: Another Way to “Fix” a Data Hazard
I
n
s
t
r.
O
r
d
e
r
add $1,
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$1,$7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix data hazards by forwarding results as soon as they are available to where they are needed
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Notes: For class handout

## Slide 32: Another Way to “Fix” a Data Hazard
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix data hazards by forwarding results as soon as they are available to where they are needed
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
I
n
s
t
r.
O
r
d
e
r
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Notes: For lecture
Forwarding paths are valid only if the destination stage is later in time than the source stage.
Forwarding is harder if there are multiple results to forward per instruction or if they need to write a result early in the pipeline

## Slide 33: Forwarding with Load-use Data Hazards
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Notes: For class handout

## Slide 34: Forwarding with Load-use Data Hazards
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Will still need one stall cycle even with forwarding
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Notes: For lecture
Note that lw is just another example of register usage (beyond ALU ops)
Need to stall even with forwarding when data hazard involves a load

## Slide 35: Branch Instructions Cause Control Hazards
I
n
s
t
r.
O
r
d
e
r
lw
Inst 4
Inst 3
beq
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards

## Slide 36: One Way to “Fix” a Control Hazard
stall
stall
stall
I
n
s
t
r.
O
r
d
e
r
beq
ALU
IM
Reg
DM
Reg
lw
ALU
IM
Reg
DM
Reg
ALU
Inst 3
IM
Reg
DM
Fix branch hazard by waiting – stall – but affects CPI
Notes: Another “solution” is to put in enough extra hardware so that we can test registers, calculate the branch address, and update the PC during the second stage of the pipeline. That would reduce the number of stalls to only one.
A third approach is to prediction to handle branches, e.g., always predict that branches will be untaken. When right, the pipeline proceeds at full speed. When wrong, have to stall (and make sure nothing completes – changes machine state – that shouldn’t have). Will talk about these options in more detail in next,next lecture.

## Slide 37: Corrected Datapath to Save RegWrite Addr
Need to preserve the destination register address in the pipeline state registers
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB

## Slide 38: Corrected Datapath to Save RegWrite Addr
Need to preserve the destination register address in the pipeline state registers
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB

## Slide 39: MIPS Pipeline Control Path Modifications
All control signals can be determined during Decode
  and held in the state registers between pipeline stages
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control

## Slide 40: Other Pipeline Structures Are Possible
What about the (slow) multiply operation?
  Make the clock twice as slow or …
  let it take two cycles (since it doesn’t use the DM stage)
ALU
IM
Reg
DM
Reg
MUL
ALU
IM
Reg
DM1
Reg
DM2
What if the data memory access is twice as slow as the instruction memory?
  make the clock twice as slow or …
  let data memory access take two cycles (and keep the same clock rate)
Notes: Note that we don’t need the output of MUL until the WB cycle, so we can span two pipeline stages with the MUL hardware (so the multiplier is a two stage pipelined multiplier)

## Slide 41: Summary
All modern day processors use pipelining
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Potential speedup: a CPI of 1 and fast a CC
Pipeline rate limited by slowest pipeline stage
  Unbalanced pipe stages makes for inefficiencies
  The time to “fill” pipeline and time to “drain” it can impact speedup for deep pipelines and short code runs
Must detect and resolve hazards
  Stalling negatively affects CPI (makes CPI less than the ideal of 1)