## Slide 1: CSE 340 Computer Architecture Summer 2017 Overcoming Data Hazards
Notes: Other handouts
To handout next time

## Slide 2: Review: MIPS Pipeline Data and Control Paths
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
Notes: How many bits wide is each pipeline register?
PC – 32 bits
IF/ID – 64 bits
ID/EX – 9 + 32x4 + 10 = 147
EX/MEM – 5 + 1 + 32x3 + 5 = 107
MEM/WB – 2 + 32x2 + 5 = 71

## Slide 3: Control Settings
 | EX Stage |  |  |  | MEM Stage |  |  | WB Stage | 
 | RegDst | ALUOp1 | ALUOp0 | ALUSrc | Brch | MemRead | MemWrite | RegWrite | Mem toReg
R | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
lw | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
sw | X | 0 | 0 | 1 | 0 | 0 | 1 | 0 | X
beq | X | 0 | 1 | 0 | 1 | 0 | 0 | 0 | X

## Slide 4: Review: One Way to “Fix” a Data Hazard
stall
stall
I
n
s
t
r.
O
r
d
e
r
add $1,
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$7,$1
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix data hazard by waiting – stall – but impacts CPI

## Slide 5: Review: Another Way to “Fix” a Data Hazard
I
n
s
t
r.
O
r
d
e
r
add $1,
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$7,$1
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix data hazards by forwarding results as soon as they are available to where they are needed
sw $4,4($1)
or $8,$1,$1
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Notes: Notice that for now we are showing the forwarded data coming out of the ALU. After looking at the problem more closely we will see that it really is supplied by the pipeline register EX/MEM and will depict it as such.

## Slide 6: Data Forwarding (aka Bypassing)
Take the result from the earliest point that it exists in any of the pipeline state registers and forward it to the functional units (e.g., the ALU) that need it that cycle
For ALU functional unit: the inputs can come from any pipeline register rather than just from ID/EX by
  adding multiplexors to the inputs of the ALU
  connecting the Rd write data in EX/MEM or MEM/WB to either (or both) of the EX’s stage Rs and Rt ALU mux inputs
  adding the proper control hardware to control the new muxes
Other functional units may need similar forwarding logic (e.g., the DM)
With forwarding can achieve a CPI of 1 even in the presence of data dependencies

## Slide 7: Data Forwarding Control Conditions
EX/MEM hazard:
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs))
ForwardA = 10
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRt))
ForwardB = 10
Forwards the result from the previous instr. to either input of the ALU
Forwards the result from the second previous instr. to either input of the ALU
MEM/WB hazard:
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
ForwardA = 01
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
ForwardB = 01

## Slide 8: Forwarding Illustration
I
n
s
t
r.
O
r
d
e
r
add $1,
sub $4,$1,$5
and $6,$7,$1
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
EX/MEM hazard forwarding
MEM/WB hazard forwarding
Notes: Notice that for now we are showing the forwarded data coming out of the ALU. After looking at the problem more closely we will see that it really is supplied by the pipeline register EX/MEM and will depict it as such.

## Slide 9: Yet Another Complication!
I
n
s
t
r.
O
r
d
e
r
add $1,$1,$2
ALU
IM
Reg
DM
Reg
add $1,$1,$3
add $1,$1,$4
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Another potential data hazard can occur when there is a conflict between the result of the WB stage instruction and the MEM stage instruction – which should be forwarded?
Notes: For class handout

## Slide 10: Yet Another Complication!
I
n
s
t
r.
O
r
d
e
r
add $1,$1,$2
ALU
IM
Reg
DM
Reg
add $1,$1,$3
add $1,$1,$4
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Another potential data hazard can occur when there is a conflict between the result of the WB stage instruction and the MEM stage instruction – which should be forwarded?
Notes: For lecture

## Slide 11: Corrected Data Forwarding Control Conditions
MEM/WB hazard:
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRs)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
ForwardA = 01
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRt)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
ForwardB = 01

## Slide 12: Datapath with Forwarding Hardware
PCSrc
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
Forward
Unit
Notes: For class handout

## Slide 13: Datapath with Forwarding Hardware
PCSrc
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
Forward
Unit
ID/EX.RegisterRt
ID/EX.RegisterRs
EX/MEM.RegisterRd
MEM/WB.RegisterRd
Notes: For lecture.
How many bits wide is each pipeline register now?
ID/EX – 9 + 32x4 + 10 = 147 + 10 = 157
Control line inputs to Forward Unit EX/MEM.RegWrite and MEM/WB.RegWrite not shown on diagram

## Slide 14: Memory-to-Memory Copies
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
ALU
IM
Reg
DM
Reg
sw $1,4($3)
ALU
IM
Reg
DM
Reg
For loads immediately followed by stores (memory-to-memory copies) can avoid a stall by adding forwarding hardware from the MEM/WB register to the data memory input.
  Would need to add a Forward Unit and a mux to the memory access stage
Notes: What if lw was replaced with add $1, - is forwarding still needed? From where, to where?
What if $1 was used to compute the effective address (it would be a load-use data hazard and would require a stall insertion between the lw and sw)

## Slide 15: Forwarding with Load-use Data Hazards
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
Notes: For class handout

## Slide 16: Forwarding with Load-use Data Hazards
stall
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Notes: For lecture
The one case where forwarding cannot save the day is when an instruction tries to read a register following a load instruction that writes the same register.

## Slide 17: Load-use Hazard Detection Unit
Need a Hazard detection Unit in the ID stage that inserts a stall between the load and its use
ID Hazard Detection
if (ID/EX.MemRead
and ((ID/EX.RegisterRt = IF/ID.RegisterRs)
or (ID/EX.RegisterRt = IF/ID.RegisterRt)))
stall the pipeline
The first line tests to see if the instruction now in the EX stage is a lw; the next two lines check to see if the destination register of the lw matches either source register of the instruction in the ID stage (the load-use instruction)
After this one cycle stall, the forwarding logic can handle the remaining data hazards

## Slide 18: Stall Hardware
Along with the Hazard Unit, we have to implement the stall
Prevent the instructions in the IF and ID stages from progressing down the pipeline – done by preventing the PC register and the IF/ID pipeline register from changing
  Hazard detection Unit controls the writing of the PC (PC.write) and IF/ID (IF/ID.write) registers
Insert a “bubble” between the lw instruction (in the EX stage) and the load-use instruction (in the ID stage) (i.e., insert a noop in the execution stream)
  Set the control bits in the EX, MEM, and WB control fields of the ID/EX pipeline register to 0 (noop). The Hazard Unit controls the mux that chooses between the real control values and the 0’s.
Let the lw instruction and the instructions after it in the pipeline (before it in the code) proceed normally down the pipeline

## Slide 19: Adding the Hazard Hardware
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
Notes: For class handout

## Slide 20: Adding the Hazard Hardware
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead
Notes: For lecture
In reality, only the signals RegWrite and MemWrite need to be 0, the other control signals can be don’t cares.
Another consideration is energy – where clock gating is called for.

## Slide 21: Next Lecture and Reminders
Next lecture
  Reducing branch costs
    Reading assignment – PH, Chapter 6.6 and 6.8